## Slide 1: Introduction to Computers and Programming

## Slide 2: Number Systems

## Slide 3: Decimal vs Binary vs Hex
Traditional numbers are in base 10 (decimal)
Computers operate in base 2 (binary)
Any number can be converted into a different base
Hex is base 16. Each hex digit represents 4 binary digits, so hex is shorthand for binary

## Slide 4: Basic Computer Architecture

## Slide 5
Central Processing Unit (CPU) aka the “core”
Inputs (mouse, keyboard, camera)
Hard Drive (archive of files, programs, etc., saved when computer is turned off)
Random Access Memory (RAM)
(memory for working files, erased when computer is turned off)
signals
Outputs (monitor, speakers, projectors, lights)
signals
Data
Data
Notes: Data In vs Data Out

## Slide 6: Peripherals: Outputs
Examples: Mouse, keyboard, trackpad, camera, disk drive
  Inputs gather information and help the processor make decisions. They are the interface for how humans tell the computer what to do.
Peripherals: Inputs
Examples: Screen, speakers, lights, printer
  Outputs display the results of the computer in ways humans can understand

## Slide 7: Memory (3 kinds)
Hard Drive (Permanent)
  Stores permanent files such as: pictures, videos, program files, the operating system, etc.
  Usually 128/256/512 GB or 1/2/4 TB
RAM aka Random Access Memory (Temporary)
  Faster than Hard Drive
  Used for running programs
  Usually 2/4/8 GB
Registers (Temporary)
  Part of the central processor
  Each register can only hold 1 number
Hard Drive RAM

## Slide 8: Hierarchy of Programming

## Slide 9: Point and click programming
High level
language
Machine code
(individual instructions)
Logic gates
Environments: Excel, Powerpoint, etc…
Languages: C, C++, Java, R, Python, HTML
Example: int counter = 1; (find memory to store an integer
variable, name it counter, and set it equal to 1)
Language: Assembly
Example command in Hex (base 16): F3A8
Same command in Binary (base 2): 1111 0011 1010 0100
Universal Gates: AND, OR, NOT
Example: ABC (A and B and C)
Example: A+B+C (A or B or C)

## Slide 10: Logic Gates 1: Transistors
Basic component of all computers
Allow for electricity to flow when certain conditions are met
Can be linked to form more complex structures
2 kinds of transistors N and P
Transistor
Inverter made from 2 transistors
AND Gate made from 6 transistors

## Slide 11: Logic Gates 2: Boolean Algebra
Use Boolean Algebra where variables are either 1 or 0
Inputs are either 1 (typically 5 Volts = “Logic 1” or “Logic High”) or 0 (0 Volts = “Logic 0” or ”Logic Low”)
Can use these AOI gates to build any logical expression
A DECODER will only give voltage to 1 output (D). The output that gets voltage depends on the inputs (A)
Boolean Logic
Notes: Explain voltage as water pressure.

## Slide 12: Point and click programming
Machine code (individual instructions)
Logic gates
Environments: Excel, Powerpoint, etc…
Languages: C, C++, Java, R, Python, HTML
Example: int counter = 1; (find memory to store an integer
variable, name it counter, and set it equal to 1)
Language: Assembly
Example command in Hex (base 16): 0xF3A8
Same command in Binary (base 2): 1111 0011 1010 0100
Universal Gates: AND, OR, NOT
Example: ABC (A and B and C)
Example: A+B+C (A or B or C)
High level
language

## Slide 13: Machine Code 1: Registers (hardware)
Store numbers (1 number per register)
Hold data until they get a signal to store new data
Think of them like whiteboards that can only have 1 number on them
Example of a 4-bit register
D0 through D3 are the input numbers
CP is the clock pulse. It tells the registers when to save new numbers
Q0 through Q3 are the outputs. These get sent to the CPU (brain of the computer)
Can hold any number between 0 and 24-1
Connecting a decoder to registers helps a CPU pick which registers to use

## Slide 14: Machine Code 2: Instructions (software)
Instructions that tell the computer what operation to do, what data to use, and where to store the result.
Example code in Hexidecimal: 0xF3A8
Same command in Binary: 1111 0011 1010 0100
F 3 6 8
F = operation or “opcode” (ex. Addition)
3 = first source register (R3)
6 = second source register (R6)
8 = target register (R8)
This command would add the numbers in register 3 and register 6 and store the result in register 8
Sample list of Instructions

## Slide 15: Point and click programming
Machine code
(individual instructions)
Logic gates
Environments: Excel, Powerpoint, etc…
Languages: C, C++, Java, R, Python, HTML
Example: int counter = 1; (find memory to store an integer
variable, name it counter, and set it equal to 1)
Language: Assembly
Example command in Hex (base 16): 0xF3A8
Same command in Binary (base 2): 1111 0011 1010 0100
Universal Gates: AND, OR, NOT
Example: ABC (A and B and C)
Example: A+B+C (A or B or C)
High level
language

## Slide 16: Basic Languages 1: Styling/Markup Languages
Languages: HTML, CSS, XML etc.
  Takes data and displays it an a certain way
  Does not edit data
  Used for creating tables, bolding/italicizing, creating hyperlinks, etc..
Uses
  Webpage design
  Information displays
  Help humans interpret/interact with data

## Slide 17: Basic Languages 2: General Purpose Languages
Examples: C, C++, Java, R, Python, etc…
  Math/logic based
  Takes inputs to generate outputs
  Changes data/files
Low level languages
  Low level languages create few computer instructions for each line of code
High level languages
  High level languages create many computer instructions for each line of code
The start of this program asks for the user to input 2 numbers, then it calculates the difference and outputs it to the screen a couple lines down
Sample C++ code
Notes: This is where most computer programming happens

## Slide 18: Point and click programming
Machine code
(individual instructions)
Logic gates
Environments: Excel, Powerpoint, etc…
Languages: C, C++, Java, R, Python, HTML
Example: int counter = 1; (find memory to store an integer
variable, name it counter, and set it equal to 1)
Language: Assembly
Example command in Hex (base 16): 0xF3A8
Same command in Binary (base 2): 1111 0011 1010 0100
Universal Gates: AND, OR, NOT
Example: ABC (A and B and C)
Example: A+B+C (A or B or C)
High level
language

## Slide 19: Point and Click/Scripted Programming
High level programs automatically create written code
Limits the need to write in base languages
It’s the fastest way to build tools to manipulate and present data
This program takes big chunks of code and simplifies them down so a coder can quickly make a game
Excel has preprogrammed plots and will automatically generate graphs with the push of a button

## Slide 20: How Computers Work

## Slide 21: Internal clock
Processors have a “speed” at which they operate (ex. 2.4 GHz)
  2.4 GHz means the processor can do 2.4 Billion things per second
  Having multiple cores means a computer can do multiple things at once
Do command #2019
Do command #2020
Ex. 240 picoseconds

## Slide 22: Computer Instructions
Every clock pulse, a new instruction is read and executed.
  Arithmetic instructions: Addition, subtraction, multiplication, division, comparing numbers, setting values
  Flow control instructions: Branching or conditional branching (jumping to a new instruction)
Each line of computer code is an instruction, with a unique address
Line address

## Slide 23: How Basic Code becomes Machine Language

## Slide 24: Compilers
A compiler is a program that turns a code in a certain language into a lower level code.
  Generally it takes more lines of code to do the same operations in a lower level language
  Ex. GCC is the name of a compiler that turns C/C++ code into machine code

## Slide 25: Anything Else?